HDOS/NET Reference Manual
February 25, 2023

## Introduction
This document describes details of an implementation of Networking on HDOS.

TODO: Add network printer support.
## Commands
### NETSTAT
Display status of network and mappings.
### NETWORK
Change network mappings.
### NETDIR
List files on a networked device.
### NETDEL
Delete files on a networked device.
### NETREN
Rename a file on a networked device.
## Device Driver
The device driver, “NW”, uses the HDOS “non-directory” device flag to achieve a partial file-oriented interface. HDOS does not fully support all features desired for networked files and devices, so the “Device Specific Functions” interface is also used for additional features. The basic driver will intercept .OPEN, .CLOSE, .READ, and .WRITE system calls on networked files. This does not include .POSIT, .DELET, .RENAM, .CHFLG, or .LINK. Additional festures are added by special programs.
The driver keeps a Network Configuration Table, similar to CP/NET except that it only maps 8 units (drives) and each unit’s entry is 4 bytes long. These mappings may be displayed using the NETSTAT.ABS utility and altered using NETWORK.ABS. The first byte of each entry is the remote server node ID, or 0ffh is it is not mapped. The next three bytes contain the device name and unit (in ASCII) on the remote server.
### Device Specific Functions
The following functions are added by calling the device driver entry with A=DC.DSF and C having the function number. Generally, this function number is the same as the corresponding HDOS system call. There are also some new functions added to support getting a directory listing.
C=.CHFLG D=bits E=mask HL={def-blk, file-string}
Change the flags on the file. Not all flags are supported on the server. Write protect should always work. SYS may not if the server does not support additional permissions on files. {def-blk, file-string} is an area that contains two addresses, first is the default block and second is the file string.

C=.POSIT B=channel DE=sector
Set the file pointer to sector. The channel must be for an open, networked file.

C=.RENAM DE=def-blk HL={old-file-string, new-file-string}
Rename the file. .DECODE will be applied to both old-file-string and new-file-string and must describe a network device unit.

C=.DELET HL=file-spec
Delete file(s). file-spec is similar to the results of the .DECODE system call, without the reserved fields, except that it may contain wildcards (‘*’ must be expanded to ‘?’).

C=.LINK DE=def-blk HL=file-string
This function is not implemented. It remains to be seen if it can be. On the network side, this consists of .OPENR, .READ, and .CLOSE. HDOS has other requirements for loading and starting a program which may not be accessible/adaptable.

C=.SERF (11H) DE=buffer HL=file-spec
Search First. CY is set for errors, with A containing the error code (including EC.EOF). On success, buffer will be filled with a 23-byte directory entry. This entry will differ from a local HDOS directory entry in that the DIR.FGN and DIR.LGN bytes will contain the size of the file in 256-byte sectors, little-endian (16-bit value). file-spec is as specified for .DELET.

C=.SERN (12H) DE=buffer
Search Next. Same results as for Search First.

C=.NTCFG (45H)
Get Network Configuration Table. Returns HL=address of table.

## Network Messages
The network message format is similar to the CP/NET message format, except the format byte 10H is used for requests and 11H for responses. The general message format is:
FMT	DID	SID	FNC	SIZ	payload

Where FMT is the message format as specified by CP/NET, using 10H and 11H for HDOS. DID and SID are the destination and source node IDs, respectively. The response swaps the node IDs compared to the request. FNC is the function to be performed. SIZ is the size of the payload, minus 1. Payload is always at least one byte.
### .READ
10H	DID	SID	04H	00H	CHA

11H	DID	SID	04H	00H	EC

11H	DID	SID	04H	FFH	256-bytes

### .WRITE
10H	DID	SID	8xH	FFH	256-bytes

11H	DID	SID	8xH	00H	EC

8xH: Channel number with high bit set
### .OPENR, .OPENW, .OPENU
10H	DID	SID	FNC	0EH	CHA	file-spec

11H	DID	SID	FNC	00H	EC

### .CLOSE
10H	DID	SID	26H	00H	CHA

11H	DID	SID	26H	00H	EC

### .POSIT
10H	DID	SID	27H	02H	CHA	sector

11H	DID	SID	27H	00H	EC

### .DELET
10H	DID	SID	28H	0DH	file-spec

11H	DID	SID	28H	00H	EC

### .RENAM
10H	DID	SID	29H	1BH	old-file-spec	new-file-spec

11H	DID	SID	29H	00H	EC

### .CHFLG
10H	DID	SID	30H	0FH	mask	bits	file-spec

11H	DID	SID	30H	00H	EC

### .SERF
10H	DID	SID	11H	0EH	vers	file-spec

11H	DID	SID	11H	00H	EC

11H	DID	SID	11H	16H	dir-entry

### .SERN
10H	DID	SID	12H	00H	---

11H	DID	SID	12H	00H	EC

11H	DID	SID	12H	16H	dir-entry