HDOS FTP Reference Manual
April 5, 2023

## Introduction
This document describes details of an implementation of Networking on HDOS using a simplified version of “ftp” designed for HDOS and use with CP/NET servers. As such, the program operates as a network-oriented command shell.

If “ftp” is invoked with a hex number argument, it will begin by performing an “open” command for that argument (the remote server network ID). In either case, “ftp” then prompts the user for commands.

Commands must be entered in lower-case. Arguments are generally not case-sensitive. The command “help” will display a list of available commands.
## Commands
open sid
Opens a connection (socket) to the specified server ID, designated as a hexadecimal number between 0 and FE. The server ID must have been set-up in the network configuration (e.g. see wizcfg for WIZnet networks). There must not be a connection open.
close
Close the current connection. This must be done in order to open a new connection (e.g. to a different server).
quit
Quit ftp, closing any connection.
cd drive
Change the remote drive. Since remote servers are CP/NET, drive is designated using CP/M nomenclature A: through P:. Default is A:. Resets to default on opening a connection.
lcd device
Change the local HDOS device. Default is SY0:. Resets to default on opening a connection.
status
Display connection status, including current remote drive and local HDOS device.
dir [pattern]
List remote files, filtered by pattern.
size file
Show size of (remote) file, in 1K resolution.
get remote-file [local-file]
Download remote-file, optionally renaming to local-file. If remote-file contains wildcards then local-file is not allowed.
put local-file [remote-file]
Upload local-file, optionally renaming to remote-file. If local-file contains wildcards then remote-file is not allowed. TBD: should file overwrite be allowed?
delete file
TBD: should this be allowed?
rename old-name new-name
TBD: should this be allowed?

## More